## Slide 1: Signals & Systems
Predicting System Performance
February 27, 2013

## Slide 2: Outline
System functions: primitives and compositions
Modes of feedback systems
Finding and interpreting poles
Reading: Chapter 5.5 – 5.7 of Digital World Notes

## Slide 3: Performance analysis
We can quantify the performance of a system by characterizing the signals that the system generates.

## Slide 4: Analyzing systems
Our goal is to develop representations for systems that facilitate analysis.
Examples:
Does the output signal overshoot? If so, how much?
How long does it take for the output signal to reach its final value?

## Slide 5: System functions
Any LTI system is completely characterized by the relationship between the input signal X and the output signal Y .
We call this relationship,
the system function. It is independent of any particular input signal, just as a mathematical function or a Python procedure is an entity, independent of its arguments.
System functions for LTI systems are always
ratios of polynomials in R.

## Slide 6: System functions for LTI systems
Ratio of polynomials in R:
Persistent part of response of such a system is associated with de- nominator.

## Slide 7: System functions: Why do we care
PCAP system on system functions makes it easier to combine models than manipulating systems of operator equations.
System functions expose important analytic properties of the system.

## Slide 8: PCAP: Primitive SFs

## Slide 9: Combining SFs: Sum
The system function of the sum of two systems is the sum of their system functions.

## Slide 10: Combining SFs: Cascade
The system function of the cascade of two systems is the product of their system functions.

## Slide 11: Combining SFs: Negative feedback
Concentrate on negative feedback and Black's formula:

## Slide 12: Wall finder
Control the robot to move to desired distance from a wall.

## Slide 13: Use composition to find SF

## Slide 14: Wall finder
The behavior of the system depends critically on KT.

## Slide 15: Predicting properties of system behavior
Consider how the system behaves given input signals with different properties:
• Unit sample (this lecture)
• Transient : finitely many non-zero samples
• Bounded : exist values u, l such that l < x[n] < u for all n
Understanding unit-sample response is the basis for understanding
response to more complex signals.
We can predict system behavior (slowly) by simulating any system.
We can quickly predict long-term behavior of the unit-sample response based on the denominator of the system function.

## Slide 16: Feed-forward systems
Output has no dependence on previous outputs
Unit-sample response is finite sum of scaled, delayed unit-samples
Unit-sample response is transient: finitely many non-zero values

## Slide 17: Feedback systems: First-order case

## Slide 18: Feedback

## Slide 19: Feedback: Cyclic signal flow paths
Feedback implies cyclic signal flow paths.

## Slide 20: Feedback: Cyclic signal flow paths
Feedback implies cyclic signal flow paths.

## Slide 21: Feedback: Cyclic signal flow paths
Feedback implies cyclic signal flow paths.
All cyclic paths must contain at least one delay.

## Slide 22: Unit sample response: Geometric growth
If traversing the cycle decreases or increases the magnitude of the signal, then the output will decay or grow, respectively.

## Slide 23: Unit sample response: Geometric growth
These system responses can be characterized by a single number (the pole), which is the base of the geometric sequence.

## Slide 24: Cohort Question 1

## Slide 25: Geometric growth

## Slide 26: Second-order systems
The unit-sample response of more complicated cyclic systems is more complicated.

## Slide 27: Second-order systems
The unit-sample response of more complicated cyclic systems is more complicated.
Not geometric. This response grows then decays.

## Slide 28: Second-order systems: Additive decomposition
This system function can be written as a sum of simpler parts.

## Slide 29: Additive decomposition: partial fraction expansion

## Slide 30: Second-order systems: Additive decomposition

## Slide 31: Second-order systems: Additive decomposition

## Slide 32: Sum of geometric sequences
Mode with biggest base eventually governs behavior

## Slide 33: More dramatically

## Slide 34: Analysis of more complicated systems
Rational polynomials can be realized with block diagrams of the following form:

## Slide 35: Analysis of more complicated systems
Modes can be identified by expanding system functional in partial fractions.

## Slide 36: Analysis of more complicated systems
Modal decomposition provides an alternative block diagram.
The upper part is cyclic; the lower part is acyclic.

## Slide 37: Easy way to find poles

## Slide 38: Complex Roots
What if a root has a non-zero imaginary part?
Factor theorem: express a polynomial as a product of factors, with one factor associated with each root of the polynomial.
Fundamental theorem of algebra: a polynomial of order n has n roots. The roots can have imaginary parts.
How does a mode from a complex root behave?

## Slide 39: Complex Poles
Difference equations that represent physical systems (e.g., population growth, bank accounts, etc.) have real-valued coefficients.
Difference equations with real-valued coefficients generate real-valued outputs from real-valued inputs.
But they might still have complex poles.

## Slide 40: Representing complex numbers

## Slide 41: Complex Poles

## Slide 42: Complex Poles

## Slide 43: Convergence and Divergence

## Slide 44: Complex Roots
Self Reading: Complex Conjugate Root Theorem:
http://en.wikipedia.org/wiki/Complex_conjugate_root_theorem

## Slide 45: Complex Roots
If we pair the factors corresponding to complex-conjugate roots, the resulting polynomial has real-valued coefficients.

## Slide 46: Complex modes, Real results

## Slide 47: Complex modes, Real results

## Slide 48: Complex modes, Real results

## Slide 49: Complex modes, Real results

## Slide 50: Cohort Question 2

## Slide 51: Cohort Question 3

## Slide 52: Poles and convergence
The dominant pole is the pole with the largest magnitude.
If the dominant pole has magnitude > 1, then in response to a bounded input, the output signal will be unbounded.
If the dominant pole has magnitude < 1, then in response to a bounded input, the output signal will be bounded; in response to a transient input, the output signal will converge to 0.
If the dominant pole has magnitude 1, then in response to a bounded input, the output signal will be bounded; in response to a transient input, it will converge to some constant value.

## Slide 53: Poles and periodicity
The dominant pole is the pole p = a + bj with the largest magnitude.
Assume that |p| is not 1 or 0 and Y = Hδ, there exists a time t such that:
If b = 0, a > 0, y[n] is monotonically decreasing or increasing.
If b = 0, a < 0, y[n] is alternating signs.
Otherwise, oscillating

## Slide 54: This Week
Readings: Chapter 5.5-5.7 of Digital World Notes (mandatory!)
Cohort Exercises & Homework: Practice on LTI systems (note the due dates & times)
Lab: Analyzing robot control system for stability